Concepts
Main Concerns
1. Reliability
2. Security
3. Real-Time Behavior
4. Energy Efficient
Embedded Systems are Reactive (Automata)
1.Waits for Input
2. Performance Computations
3. Generate Outputs
System Model
Inputs: Sensors
Outputs: Actuators
Computations: Processing Elements
In this Course:
1. How to pick appropriate PE (Processing Element)
2. How to interface with sensors and actuators.
3. how to program your PE.
Design
- Application
- Requirements
- characterestics
- Chanllenges
    - Dependability
    - Effeciency
    - Real-time Constraints
Attributes of Dependability
- Reliable
- Available
- Maintainable
- Safe
- Secure
Efficiency
- Energy Efficiency - Number of instructions per joule
- Code Size
- Weight
- Cost
Processors -- Least Efficients
ASIC -- Most Efficient
Hardware == Software
Design-Flow
- Idea
- Specs
- Repository
- Iteration
- Evaluation
- Validation
Input-Output I/O
- Peripherals
- Serial / parallel
    - SPI
    - GPIO
- Analog/Digital
Reading Input
- Polling / Interrupts
- UART
- DAC ADC
- Direct Memory Access
- USB
- Synchronous / Asynchronous
- Full Duplex / half duplex
- resolution of ADC
- ADC - Successive Approximation
- DAC - PWM
- Noise in sensor measurements
- Sampling

ASIC – Application Specific Integrated Circuits
Device that is created with specific purpose in mind.
http://www.eetimes.com/author.asp?doc_id=1322856

 Serial / Parallel Ports
Serial ports transmit data 1 bit at a time. While parallel ports transmit data 8 bits at a time. Parallel transmission is faster, but more complicated, because each bit travels along its own data path. Serial transmission is normally slower but simpler, because each bit shares a data path.

The RS232 standard is used by many different manufacturers of devices. Some common devices that use the serial port connection are flat screen monitors, GPS receivers, bar code scanners and satellite phones or modems.

The parallel port is virtually synonymous with being a printer port. Other devices that communicate with a parallel port are zip drives, scanners, joysticks, external hard drives and webcams. Today, the parallel port has been replaced by the new USB port for connecting these same devices to the computer.

Direct Memory Access (DMA)
y every member of a population or group.  Rath
https://www.cs.umd.edu/class/sum2003/cmsc311/Notes/Memory/dma.html
Now imagine that the I/O device wants to store a lot of data to memory. Perhaps you have just taken some pictures on a digital video camera, and want to store this information.
One way to do this is to alert the CPU that the I/O device wants to store data to memory. These are the steps that might be taken.
- CPU sends signal to I/O device to put data on data bus.
- I/O device places data on data bus, and signals it has done so.
- CPU reads in the data into a register, and signals the I/O device that it has finished reading the data.
- CPU signals memory that it is ready to write data to memory.
- CPU places address and data on data bus.
- Memory writes data from data to some memory location.
- Memory signals CPU it has written data.
Thus the data flows from the I/O device to the CPU, and from the CPU to memory.

DMA
It should seem obvious that there is a quicker way to put the data in memory. After all, these are lecture notes on "Direct Memory Access", so the idea is to access memory directly, and avoid the CPU as the middle man.
After all, how can memory who is sending signals to it? How does it know that the CPU sends signals, instead of the device itself.
If the I/O device generates all the signals that the CPU does, then the I/O device can bypass the step where the data transfers to the CPU, thus, potentially doubling the speed.
ADC – Succesive Approximation
If we consider the example of an analog input value of 0.425 V and a voltage reference of 1 V, we can approximate the output of an 8 bit ADC as follows:
1. Set first bit of 8 bit output to 1 so output to DAC is 0.5
2. 0.5 subtracted from 0.425 is less than 0, so set the first bit of output to 0
3. Set second bit of 8 bit output to 1, so output to DAC is 0.25
4. 0.25 subtracted from 0.425 is greater than 1, so second bit of output is 1
5. Set third bit of 8 bit output to 1, so output to DAC is 0.375
6. 0.375 subtracted from 0.425 is greater than 1, so third bit of output is 1
This process is repeated for all 8 bits until the output is determined to be:
01101100

Code:

%8−bit digital output is all zeros
digital output = zeros(1,8);
%Normalised to one for example
reference voltage = 1;
for i=1:8
 %current output bit set to 1:
 digital output(i)=1;
 compare threshold = 0;
 %Output digital output in current form to DAC:
 for j=1:i
  compare threshold = compare threshold+digital output(j)*reference voltage/(2ˆj);
 end
 %Comparator compares analog input to DAC output:
 if (input voltage−compare threshold<0)
  digital output(i)= 0;
 end
end
Sampling

USB – Universal Serial Bus
http://www.geoffknagge.com/uni/elec101/essay.shtml
http://www.eeherald.com/section/design-guide/esmod14.html